## Slide 1: LCOE Review
By: Bill

## Slide 2: What is LCOE / why does it matter
LCOE is the sum of three key components
  Capital cost amortized over life of plant + O&M cost per year
  Variable costs
  Fuel costs
Allows the comparison of different technologies of unequal life spans, project size, different capital cost, risk, return, and capacities
Useful investment metric for comparing new options
Can be thought of as
  Long run average cost
  Breakeven cost over an assumed financial life and duty cycle
  Long run marginal cost of power plant
  The minimum price of electricity sold to the grid

## Slide 3: What are the Drawback
Assumes a kWH is the same as any other kWH
  This can artificially favor VRE compared to baseload
Hard to compare a new plant to an existing plant
Not useful when looking at energy systems because time factors are not included
  Supply has no obligation to meet demand
Does not take storage costs into account
Requires an assumed interest rate for future dollars
  This can negatively impact plants with longer lifecycles like nuclear
Not every quoted LCOE is calculate the same
  LCOE doesn’t always take capacity factor into account
  Sometimes measures total life and sometimes is annualized
  Sometimes MWH instead of kWH

## Slide 4: How Can We Fix it
Get more data
Calculate LCOE from scratch as opposed to pulled from other sources
Require storage be included VRE over a certain capacity size after a certain VRE penetration percentage
Automate and update metrics more frequently
Be more transparent with calculations
Favor baseload power after certain VRE penetration percentage
Use LCOE, LCOS, or LACE when applicable in the modeling loop

## Slide 5: Key factors
Construction time
Regulatory hurdles
Interconnection challenges
Capital costs
Capacity – capacity factor -> energy production
Maintenance and Operation costs – fixed costs
Variable costs (scale with plant output)
Fuel costs – a specific variable cost
Expected lifetime – std dev(min, max)
Discount rate for value of future money
Potential policy updates and changes
Storage costs or downtime factor
Startup/shutdown costs
Comparable existing generation types and prices
Potential revenue
Ideation
Operation
LCOE
LCOS
LACE
Notes: Use LCOE – tag external factors besides it
- regulation
- storage
- time deferred rates
- competition – LACE
Purchased kWh
ISOs not super competitive
Factors to affect variable renewables – demand side management – load shifting
How much increasing capacity affects demand
Demand sensitivity to retail energy cost – don’t need to
  Direct impact of cost on demand and indirect impacts
  Asymptote of demand is almost effectively infinite
  If all humans had us energy footprint -> theoretical max energy demand
Equivalent of app store for energy
VRE Penetration percentage
% investment shortsighted vs long term focused

## Slide 6: Appendies

## Slide 7: Sources
https://www.energy.gov/sites/prod/files/2015/08/f25/LCOE.pdf
https://www.nrel.gov/analysis/tech-lcoe.html
https://www.nrel.gov/analysis/crest.html
https://www.nrel.gov/docs/legosti/old/5173.pdf
https://commercialsolarguy.com/you-know-lcoe-but-how-about-lcos-energy-storage-analysis-from-lazards/
https://www.pnnl.gov/lcos-estimates
https://www.eia.gov/outlooks/aeo/pdf/electricity_generation.pdf

## Slide 8: Hypothetical Modeling Flow
Estimate demand, based on supply calculate a price (factor in PTC for renewables), if price(LACE) is higher than LCOE add generation capacity of certain types, based on new supply recalculate price, at new price which sectors would grow demand
Remove generation or demand that is no longer economically viable
Add time lag for construction of both demand and supply nodes
  Time to construct power plant of X capacity
  Time to construct data center
  Time to construct EV super charger
  Time to construct X miles of transmission – what if HV
Loop cycle to a max of X times per balancing era

## Slide 9: Building a new plant, factors to consider
Risk
Potential gain
Time to get return on investment
https://www.youtube.com/watch?v=UC_BCz0pzMw&t=836s
Construction costs, fuel cost, construction time
Revenue costs are very complicated to calculate